## Slide 1: Control Logic
Morris Mano Chapter 10

## Slide 2: Introduction
Think of any algorithm (keep it simple, the basic stuff)
Now implement that in hardware
Not so simple, is it?
This is where control logic comes in.

## Slide 3: Designing hardware using control logic
- Write the algorithm
- Form a flowchart from the algorithm
- Form a state diagram from the flowchart
- Choose one of the four methods of control organization
- Generate control signals accordingly

## Slide 4: Methods of control organization
- One Flip-flop per state method
- Sequence Register and Decoder Method
- PLA control
- Microprogram control

## Slide 5: One FF per state
- Recall that we form a state diagram from the flowchart of an algorithm.
- We can treat each state as a flip-flop
- So will have the same number of flip-flops as the number of states.
  E.g. if we have 10 states, we will have 10 flip-flops
- At a time, only one flip-flop (meaning one state) will be active.
- Using the active flip-flop, we will generate control signals according the requirement of the state

## Slide 6: Sequencer Decoder Method
- Minimize the number of FFs.
- For n states, we can use FFs. So for 16 states, we need only 4 FFs.

## Slide 7: Addition-Subtraction

## Slide 8: Problem Statement
- Implement the hardware for addition/subtraction of two fixed point binary numbers represented in sign-magnitude form
- What is the Sign-magnitude form?
- We have 1 bit to represent the sign of the number. But we don’t store the other bits in 2’s complement form. Rather, we keep the magnitude as it is.
- For example, if we have 4 bit numbers (1 sign bit + 3 bit magnitude) –
  3 = 0 011
  -3 = 1 011

## Slide 9: Equipment Configuration

## Slide 10: Derivation of the algorithm
- Eight possible combinations:
But, is actually equivalent to
So is to
Thus we have 4 possible combinations
  So we only need to do addition if we just change the sign of B for subtraction.

## Slide 11: Derivation of algorithm
if A ≥ B (Cout = 1) if A < B(Cout = 0)
(+A) + (+B) = + (A+B)
(+A) + (-B) = +(A-B) - (B-A)
(- A) + (+B) = - (A-B) +(B-A)
(- A) + (-B) = - (A+B)

## Slide 12: Algorithm
If subtraction, complement the sign of B
If the sign of A and B are equal- A = A + B, E = Cout , end of process
Else –
  A = A – B, E = Cout
  Check if the result (A) is positive, if so set E = 0 and end
  Otherwise change A to –A by performing 2’s complement. Also complement the sign of A, and end process.
  Question: We are using sign-magnitude form here. But why did we use 2’s complement to change A to –A?

## Slide 13: Flowchart
Initial State x=1
Bs=Bs’
As:Bs
A=A+B’+1
E=Cout
A=A+B
E=Cout
E
A=A’
E=0
A=A+1
As=As’
qa=1
qs=1
!=
=
1 (A>=B)
0(A<B)
T0
T2
T1
T3
T4
T6
T5
T7

## Slide 14
Initial State x = 1
qs = 1
qa = 1
≠
=
= 0
= 1

## Slide 15: State Diagram
T7
T4
T3
T1
T2
T6
T5
T0
qs=0
qa=0
S=1
qa=1
S=0
qs=1
E=1
E=0

## Slide 16: Control Signals
 | X | S2 | S1 | S0 | Cin | L | y | z | w
T0:Ininitial state x=1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
T1: Bs = Bs’ | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
T2: nothing | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
T3: A =A+B E=Cout | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0
T4: A+B’+1 E=Cout | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0
T5: E=0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
T6: A=A’ | 0 | 1 | 1 | 1 | 0 | 1 | 0 | 0 | 0
T7:A=A+1 As=As’ | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 0

## Slide 17: Boolean Functions for control
Flip-flop input functions
DT0 = qa‘qs’T0 + T3 + ET5 + T7
DT1 = qsT0
DT2 = qaT0 + T1
DT3 = S’T2
DT4 = ST2
DT5 = T4
DT6 = E’T5
DT7 = T6
Output control functions
x = T0
s2 = T6
s1 = T4 + T6
s0 = T3 + T6
Cin = T4 + T7
L = T3 + T4 + T6 + T7
y = T1
z = T7
w = T5

## Slide 18: Multiplication

## Slide 19: Problem Statement
- Perform multiplication of two fixed point binary numbers in sign-magnitude representation
- Each magnitude is k bits long
- So the product can be up to 2k bits long.

## Slide 20: Concept
23 10111 multiplicand
19 x 10011 multiplier
---- --------
10111
10111
00000
00000
10111
--------------
437 110110101 product

## Slide 21: Concept (cont.)
- Look at successive bits of the multiplier, LSB first.
- If the multiplier bit is a 1, the multiplicand is copied down, otherwise zeros are copied down.
- The numbers copied down in successive lines are shifted one position to the left.
- Finally numbers are added.
- Sign of product is the XOR of the signs of multiplicand and multiplier.

## Slide 22: Concept (cont.)
- Problem of this method?
- We cannot copy down the values anywhere in hardware.
- So we change the process a bit.

## Slide 23: Solution
- Provide circuit for the summation of only two binary numbers and successively accumulate the partial products in a register.
- Instead of shifting multiplicand to the left, we shift the partial product to the right.
- When corresponding bit of multiplier is 0, there is no need to add all zeros.

## Slide 24: Example
Multiplicand: 1011 Multiplier: 1101 ------------ 1st multiplier bit = 1, add multiplicand 1011 shift right 01011 2nd multiplier bit = 0, shift right 001011 3rd multiplier bit = 1, add multiplicand 110111 shift right 0110111 4th multiplier bit = 1, add multiplicand 10001111 shift right 10001111 (product)

## Slide 25: Equipment Configuration

## Slide 26: Algorithm
Initial State x=1
P=P-1
Q1
As=Bs  Qs
A=0, E=0
P=k
A=A+B
E=Cout
P=P-1
P
AQ=shr EAQ, E=0
qm=1
0
1
=0
T0
!=0
T2
Q1T2
T1
T3

## Slide 27: State Diagram
T0
T1
T2
T3
qm=0
qm=1
Pz=0
Pz=1

## Slide 28: Data Processor

## Slide 29: Control Design

## Slide 30: Hardware

## Slide 31: Assignment
1. Implement Addition-Subtraction with Sequence Register-Decoder method.
2. Implement Multiplication with One FF per state method.